## Slide 1: JC3504 Robot Technology
Lecture 12: Localisation

## Slide 2: Outline
Markov Localisation
The Bayes Filter
Particle Filter
Kalman Filter
  Kalman Filter 1-D Example
  Kalman Filter (Simplified)
  Kalman Filter (full-version)

## Slide 3: Localisation
Localisation in robotics involves the determination of a robot's position and orientation within its environment, utilising various sensors and algorithms to enable accurate navigation and interaction with surroundings.
The primary challenge of localisation in robotics lies in achieving accurate and robust position estimation amidst dynamic environments, sensor noise, and the inherent uncertainty of real-world settings.

## Slide 4: Motivating Example
Imagine a floor with three doors, two of which are closer together, and the third farther down the corridor. Imagine now that your robot is able to detect doors i.e. it is able to tell whether it is in front of a wall or in front of a door. Features like this can serve as a landmark for the robot.

## Slide 5: Motivating Example
Given the map of the environment but no information about the robot's location, we can use landmarks to drastically reduce the space of possible locations once the robot has passed one of the doors. When a robot passes through a door, it cannot ascertain which door it has passed through, but it knows it is in front of a door; hence, its estimation of its own position is as follows.
The location possibility distribution

## Slide 6: Motivating Example
One way of representing this belief is to describe the robot’s position with three Gaussian distributions, each centred in front of a door and its variance a function of the uncertainty with which the robot can detect a door’s centre.
This is known as a multi-hypothesis belief, since we have a hypothesis stating that the robot can be in front of each door.
The location possibility distribution

## Slide 7: Motivating Example
If the robot continues to move, according to the error propagation law:
The Gaussians describing the robot’s 3 possible locations will move with the robot.
The variance of each Gaussian will keep increasing with the distance the robot moves.
The location possibility distribution

## Slide 8: Motivating Example
Assuming we trust our door detector much more than our odometry estimate, we can now remove all beliefs that do not coincide with a door.
Again assuming our door detector can detect the centre of a door with some accuracy, our location estimate’s uncertainty is now only limited by that of the door detector.
The location possibility distribution

## Slide 9: Markov Localisation
Calculating the probability to be at a certain location given the likelihood of certain observations is the same as any other conditional probability. There is a formal way to describe such situations: Bayes' Rule.
Initially, we have no knowledge of the position, so for the robot, the location follows a uniform distribution. We use represents the location distribution (we regard the space as a 1-dimention space).
The location possibility distribution
( is a uniform distribution)

## Slide 10: Markov Localisation
Then, the sensor detects a door. So is updated with . According to Bayes' Rule,
The location possibility distribution
Notes: might be the most confusing part of information we need to collect. Here, ‘loc’refers to x axis, is independent to x axis, this means the value of is the same at every point on x. So, is also a uniform distribution.
P is the distribution represented by the probability density function. The multiplication and division of two probability density functions can be expressed by 'or' and 'and' operations, but normalization is required after the calculation, because the integral of the probability density function must be 1.
𝑃(𝑑𝑜𝑜𝑟) might be the most confusing part of information we need to collect. Here, ‘loc’refers to x axis, 𝑃(𝑑𝑜𝑜𝑟) is independent to x axis, this means the value of 𝑃(𝑑𝑜𝑜𝑟) is the same at every point on x. So, 𝑃(𝑑𝑜𝑜𝑟) is also a uniform distribution.
P is the distribution represented by the probability density function. The multiplication and division of two probability density functions can be expressed by 'or' and 'and' operations, but normalization is required after the calculation, because the integral of the probability density function must be 1.

## Slide 11: Markov Localisation
Then, the sensor detects a door. So is updated with . According to Bayes' Rule,
The location possibility distribution
posterior probability
prior probability
Notes: might be the most confusing part of information we need to collect. Here, ‘loc’refers to x axis, is independent to x axis, this means the value of is the same at every point on x. So, is also a uniform distribution.
P is the distribution represented by the probability density function. The multiplication and division of two probability density functions can be expressed by 'or' and 'and' operations, but normalization is required after the calculation, because the integral of the probability density function must be 1.
𝑃(𝑑𝑜𝑜𝑟) might be the most confusing part of information we need to collect. Here, ‘loc’refers to x axis, 𝑃(𝑑𝑜𝑜𝑟) is independent to x axis, this means the value of 𝑃(𝑑𝑜𝑜𝑟) is the same at every point on x. So, 𝑃(𝑑𝑜𝑜𝑟) is also a uniform distribution.
P is the distribution represented by the probability density function. The multiplication and division of two probability density functions can be expressed by 'or' and 'and' operations, but normalization is required after the calculation, because the integral of the probability density function must be 1.

## Slide 12: Markov Localisation
When the robot moves, , the distance () can be obtained from the odometer.
Assume we want to move to , but there is an error in the odometer. So,
The location possibility distribution
Notes: and are independent, so
, and independent to x, so they can be regards as is uniform distributions.
〖𝑙𝑜𝑐〗_0 and 𝑜𝑑𝑜 are independent, so 𝑃(𝑜𝑑𝑜,〖𝑙𝑜𝑐〗_0 )=𝑃(〖𝑙𝑜𝑐〗_0 )𝑃(𝑜𝑑𝑜 )
𝑃(〖𝑙𝑜𝑐〗_0 ), 𝑃(〖𝑙𝑜𝑐〗_1 ) and 𝑃(𝑜𝑑𝑜 ) independent to x, so they can be regards as is uniform distributions.

## Slide 13: Markov Localisation
When the robot moves, , the distance () can be obtained from the odometer.
Assume we want to move to , but there is an error in the odometer. So,
The location possibility distribution
:
:
:

## Slide 14: The Bayes Filter

## Slide 15: The Bayes Filter
A Bayes Filter is a probabilistic tool for estimating the state of a system (e.g. robot location) over time, updating predictions with new evidence (e.g. sensor signal) using Bayesian inference.
To formalize our terms and notation, we will describe our robot’s motion model as the distribution given by that is, the probability of being in a particular state given that we started in state and executed action .
We can describe our sensor model as being characterized by the distribution given by , namely the probability that we would see sensor observation if we were in state .

## Slide 16: The Bayes Filter
Our goal with the Bayes filter will be to estimate our robot’s state over time (, where indicates timestep) given a history of actions and observations (sensor measurements).
We compute the belief i.e. the posterior probability of our state estimate (), given a history of actions () and sensor measurements () as:
all the historical actions and observations
Notes: is e.g. the location distribution at time t
𝛼 ̂(𝑥_𝑡 ) is e.g. the location distribution at time t

## Slide 17: The Bayes Filter
Always using all the historical data will lead to the consumption of increasing computational resources. Therefore, we want to calculate based on the information of .
We assume only depends on (Markov assumption), then:
can be regarded as a constant, .
They give:
Notes: If we don’t use Markov assumption, may depend on
If we don’t use Markov assumption, 𝑧_𝑡 may depend on 𝑢_0,…,𝑢_𝑡

## Slide 18: The Bayes Filter
This final equation is remarkable because it allows us to perform a belief update for a given state by incorporating a sensor measurement and/or a motion prediction based on an action we took.

## Slide 19: Example: Bayes Filter on a Grid
Instead of using a coarse topological map, we can model the environment as a fine-grained grid. We assume that the robot is able to detect walls around it with short-range sensors.

## Slide 20: Example: Bayes Filter on a Grid
Initially, the robot does not see a wall and therefore could be almost anywhere.
real position
estimated position

## Slide 21: Example: Bayes Filter on a Grid
The robot now moves. As soon as the robot encounters the wall, the perception update bumps up the likelihood to be higher in grid cells near walls.
real position
estimated position

## Slide 22: Example: Bayes Filter on a Grid
The robot then performs a right turn and travels along the wall until hits the wall again.
real position
estimated position

## Slide 23: Example: Bayes Filter on a Grid
The robot continuously travels along. when it reaches the gap in the wall, it is almost certain about its position.
real position
estimated position

## Slide 24: Particle Filter

## Slide 25: Particle Filter
Although grid-based Markov Localisation can provide compelling results, it can be computationally very expensive, particularly when the environment is large, and the resolution of the grid is small. This is in part due to the fact that we need to carry the probability to be at a certain location forward for every cell on the grid, regardless of how small this probability is.
An elegant solution to this problem is the particle filter.

## Slide 26: Particle Filter
Initially, we generate a set of particles, each represents a possible initial state of the robot.
real position
estimated positions and orientations
0
1
2
3
4
5
6
7
8
9

## Slide 27: Particle Filter
Every time the robot moves, we will move each particle in the exact same way, but add noise to each movement much like we would observe on the real robot. Without a perception update, the particles will spread apart farther and farther.
real position
estimated positions and orientations
0
1
2
3
4
5
6
7
8
9

## Slide 28: Particle Filter
When there is new observation data, each particle is given a weight, which reflects the degree to which the state of the particle is consistent with the observation data.
real position
estimated positions and orientations
0
1
2
3
4
5
6
7
8
9

## Slide 29: Particle Filter
Particles with low weights will be eliminated and particles with high weights will be copied.
real position
estimated positions and orientations
0
2
5
8
a
b
c
d
e
f

## Slide 30: Particle Filter
We repeat this step
real position
estimated positions and orientations
0
2
5
8
a
b
c
d
e
f

## Slide 31: Particle Filter
We repeat this step
real position
estimated positions and orientations
0
2
5
8
a
b
c
d
e
f

## Slide 32: Particle Filter
We repeat this step
real position
estimated positions and orientations
2
8
a
b
c
d
f
g
h
i

## Slide 33: Particle Filter
We repeat this step
real position
estimated positions and orientations
2
8
a
b
c
d
f
g
h
i

## Slide 34: Particle Filter
We repeat this step
real position
estimated positions and orientations
2
8
a
b
c
d
f
g
h
i

## Slide 35: Particle Filter
After a few more observations, most examples will be located near the correct location of the robot.
real position
estimated positions and orientations
2
b
h
j
k
l
m
n
o
p

## Slide 36: Kalman Filter

## Slide 37: Kalman Filter
Kalman Filter is an efficient recursive filtering algorithm used for state estimation and control of linear systems.
The Kalman filter uses a dynamic model of the system, combined with past states and current observations, to predict the current state and update the prediction to more accurately reflect the real situation.

## Slide 38: Kalman Filter
The action prediction step looks as follows:
Here, denote the Kalman Filter predicting process, denotes the previous state, and is the control input.

## Slide 39: Kalman Filter 1-D Example
We only consider the x position of a robot (denoted by ), so denotes the forward distance, and denotes the odometer reading.
Given (the prediction for ), and , Kalman Filter will find .
If there is no error/noise, we would have

## Slide 40: Kalman Filter 1-D Example
Here, we want to consider the generalised situation
The state of the robot (i.e. ) may change because of itself e.g. The robot will always turn around automatically, so we use to denote the state change.
and may have different dimensions e.g. in km, in m. we use to unify them.
They give:
If there is no error/noise, the prediction is very simple.

## Slide 41: Kalman Filter 1-D Example
When we consider the errors, , , and will differ, so that only
We temporally use denotes since we haven't taken into account yet.
Because the errors exist, Kalman Filter also predict the variance of , denoted by .
Because , so
Notes: becomes unknowable.
is observable so can be read directly.
𝑥_𝑘 becomes unknowable.
𝑧_𝑘 is observable so can be read directly.

## Slide 42: Kalman Filter 1-D Example
When we consider the errors, , , and will differ, so that only
We temporally use denotes since we haven't taken into account yet.
Because the errors exist, Kalman Filter also predict the variance of , denoted by .
donotes the process noise. It encapsulates how much uncertainty we believe exists in the dynamics of the system being modelled, between state transitions.
Again, we temporally use denotes since we haven't taken into account yet.

## Slide 43: Kalman Filter 1-D Example
Now, we want to use to correct . When the values of and are different, we need to balance who to believe more. Kalman, therefore, introduces a rate parameter to deal with the balance, such that:
represents the degree of credibility of , which is estimated from the variance of .
If the variance of is large (i.e. is large), the degree should be low, vice versa.

## Slide 44: Kalman Filter 1-D Example
Kalman use the following formulation to calculate , where is the intensity of noise :
is the measurement noise. It represents the uncertainty or the "noise" in the measurements observed from the system.
Because , the term reduces the uncertainty inherent in when it passed to , thereby also reducing the variance of :

## Slide 45: Kalman Filter 1-D Example
In summary, given , , and , Kalman Filter can be regards as a two-step process.
Prediction step predicts the next state as well as the variation .
Updating step corrects the prediction according to the observation .
So far, we introduced the Kalman Filter for single state variable (e.g. x in the example).
State
State
State
Prediction
Updating

## Slide 46: Kalman Filter (Simplified)
If there are multiple state variables, e.g., position x and velocity v, and the variables are not independent of each other, we need to consider their covariance.
NB: If the variables are independent, we just need to calculate them separately.
The covariance is represented as matrix, so the formulars of the 1-D case need to be revised.

## Slide 47: Kalman Filter (Simplified)
First, will be a vector.
may also include multiple variables, so a vector again.
Therefore, and become matrix, to be clear, we replace them with and .
They give,
For example,
1-D example
Prediction
Updating

## Slide 48: Kalman Filter (Simplified)
becomes the covariance matrix .
Because of the covariance
It gives:
is the matrix version noises.
1-D example
Prediction
Updating

## Slide 49: Kalman Filter (Simplified)
becomes a matrix , because
is the matrix version noises.
Therefore,
1-D example
Prediction
Updating

## Slide 50: Kalman Filter (Simplified)
Then we got the matrix version of Kalman Filter
Prediction
Updating

## Slide 51: Kalman Filter (full-version)
There is one thing remaining. So far, we suppose that directly reflexes all the variables of , so we can produce . However, in the real-life cases, may contain patricidal data of (e.g. contains velocity, but not).
The full-version Kalman Filter use one more matrix (called the measurement matrix) to project vectors in space to space.
So that becomes:
Here, is also replaced by , because now, is in no longer in .
NB: we cannot define a matrix which maps to , because includes more dimension than .

## Slide 52: Kalman Filter (full-version)
In , , but . Recall that is the covariance matrix, so we can use to project to by
It gives:
NB: is measurement noise covariance matrix, so it’s already for .
Then, we plug in :
By applying a pseudoinverse of , we can cancel the three . It gives:

## Slide 53: Kalman Filter (full-version)
We can use the same way to replace with from :
Then we cancel the left and right of each term:

## Slide 54: Kalman Filter (full-version)
Finally, the full-version with considering the measurement matrix:
Prediction
Updating
Usually, is called Kalman gain denoted by . So,

## Slide 55: Kalman Filter (full-version)
Finally, the full-version with considering the measurement matrix:
Prediction
Updating

## Slide 56: Kalman Filter
In summary, we started from the 1-D case, then, derived the 1-D case to n-D version. Finally, we introduced the measurement matrix to obtain the common version of Kalman Filter.
1-D version
Prediction
Updating
n-D version
Prediction
Updating
Kalman Filter
Prediction
Updating

## Slide 57: Conclusion
The primary challenge of localisation in robotics lies in achieving accurate and robust position estimation amidst dynamic environments, sensor noise, and the inherent uncertainty of real-world settings.
The Bayes filter is a probabilistic framework for dynamically updating the estimate of a system's state by combining prior knowledge with observational evidence.
The Particle Filter approximates the posterior distribution of state variables using a set of random samples (particles) and weights.
The Kalman Filter is an optimal recursive data processing algorithm that provides estimates of the internal states of a linear dynamic system from series of noisy measurements.